## Slide 1
3rd Generation Partnership Project: Study on security aspects of Unmanned Aerial Systems (UAS) (Release 17)
https://docs.google.com/spreadsheets/d/106xb9tRLKw4w7PzSc3glf-_Xsy1KfJeKIXwqN-VbRto/edit?usp=sharing
Week-3

## Slide 2: Key Issue 2: Pairing authorization for UAV and UAVC
Threats:
Pairing authorization has to be performed securely between UAV and UAVC.
3gpp system must be capable to revoke the connection of UAV to UAVC.
Security requirements:
3gpp system shall support authentication and authorization of a UAV and UAVC by UTM/USS.
3gpp system shall provide means to revoke a UAV and UAVC pairing authorization.

## Slide 3: Key Issue 3: TPAE authentication and authorization
Threats:
Without authentication and authorization, potential attackers may hijack a UAV through 3GPP
networks.
Security requirements:
The TPAE shall be authorized and authenticated by 3GPP systems.
The TPAE shall be authorized and authenticated by USS/UTM.

## Slide 4: Key Issue 7: Security of command and control (C2) communication
Threats:
The lack of C2 communication security between UAV and other parties may let the attackers to
eavesdrop and control the UAV operations.
As the UAV controller could be connected via a different PLMN or using a different access
technology with a different security policy the C2 communication security with the UAV may be
compromised via the UAV controller connection.
Security requirements:
The 3GPP system shall provide means for the USS/UTM to transport security information to the
UE to secure C2.